## Slide 1: Managing Model and Data Alternatives with the Design of Ionic Liquid Enabled Separations of High Global Warming Potential Hydrofluorocarbon Refrigerants
Bridgette J. Befort, Alejandro Garciadiego, Gabriela Franco, Edward J. Maginn, and Alexander W. Dowling
Last Updated: April 26, 2022
Grant No. 1917474
Notes: 15 minutes

## Slide 2: Sustainable solutions to HFC refrigerant phaseout are necessary
Environmental Significance
Global warming potential of HFC refrigerants
Industrial
Commercial
Residential
Market: Thousands of tons
High economic value ($5/kg)
Hydrofluorocarbons (HFCs)
HFC-32
+
HFC-125
=
R-410a
GWP: 675
GWP: 3500
GWP: 2088
Existing Technology
Infeasible due to high energy requirements or lack of separating agents
Refrigerants Environmental Data. Linde Gases AG.
Goetzler et al. US Department of Energy and Navigant Consulting. (2014).
Oak Ridge National Lab. (2005).
Haynes, W.M. Thermophysical Properties of HCFC Alternatives. (1996).
50% HFC-125
50% HFC-32
Azeotrope
Separation of low- and high-GWP HFC components from existing refrigerant mixtures is worthwhile
Novel technology is required to separate HFC refrigerant components!
Notes: The systems we will apply this work to are HFC refrigerant mixtures, like R-410a. These are scheduled for phaseout under international agreements because of their high global warming potentials. To just dispose of these would be wasteful because the individual components can be reused and recycled. However, R-410a and other refrigerants are engineered as azeotropes and so separating the components is not feasible with our current technology and we need novel solutions for how to do this.

## Slide 3: Ionic liquids enable separations of the future
Salt with low melting point and low volatility
Challenge
Opportunities for Optimization
Shiflett, M. B. and Yokozeki, A. Chimica Oggi - Chemistry Today, 24(2). (2006).
Devaki, S. J. and Sasi, R. IntechOpen. (2007).
Reuse!
Recycle!
Ionic Liquid
[bmim][PF6]
1-butyl-3-methylimidazolium hexafluorophosphate
Designer solvent
106 (conservative) ILs
IL Molecular Design
Process Design
Configuration Technology
Operating Conditions
Membranes
Extractive Distillation
Edisonian Trial & Error
Expensive
Inefficient at capturing design tradeoffs
Q=652.15 kW
What tools are necessary to exponentially increase the speed of molecular and process design?
Notes: How to do exponentially faster molecular and process design?

## Slide 4
Liquid Box
Vapor Box
Experiments
Molecular Simulations
Thermodynamic Modeling & Parameter Estimation
Mullen, Corcelli & Maginn (2018), : J. Phys. Chem. Lett.
Turnaoglu, Ritchie & Shiflett (2019), J. Chem. Eng. Data
Shiflett, M. B. and Yokozeki, A. Chimica Oggi - Chemistry Today, 24(2). (2006).
Thermophysical Property Targets & IL Design
Process Design
Technoeconomic
Analysis
Temperature
Recovery Fraction
Our data-to-design framework helps address these challenges
An integrated research strategy which leverages computational molecular and process design tools, validated by experiments, enables us to systematically address these opportunities for optimization
62c @ Monday, 11/8, 8:20 AM Sheraton Back Bay, Back Bay Ballroom C
From Data to Process Design: Modeling Azeotropic Separation of High Global Warming Potential Hydrofluorocarbon Refrigerants Using Ionic Liquids

## Slide 5: Experimental data is available at a variety of conditions
IGA: Gravimetric Gas and Vapor Sorption Analyzer
XEMIS: Next Generation Gravimetric Sorption Analyzer
Binary measurements: IL and one HFC
Ternary measurements: IL and two HFCs
Yokozeki, A., & Shiflett, M. B. (2010). J. Supercrit. Fluids.
Baca, K. Olsen, G. Matamoros Valenciano, L. Bennet, M. Haggard, D. Befort, B. Garciadiego, A. Dowling, W. Maginn, E. Shiflett, M. Sus. Chem. & Engr. (2021)
[emim][Cl]
[hmim][I]
[hmim][Br]
[pmim][Cl]
[bmim][Cl]
[hmim][Cl]
[P14,6,6,6][Cl]
1 IL @ varying temperatures
[pre-2015]
Multiple ILs @ 1 temperature
[2015-present]

## Slide 6: Multiple thermodynamic models are available for modeling binary solubilities for HFC and IL mixtures
Asensio-Delgado, S., et al. (2021). Sep. and Pur. Tech.
Significance
Various HFC/IL mixtures may require different thermo models
Choice of model matters in thermo community  physical justification
+ Activity Coefficient
+ SAFT
+ …
Cubic EoS
Mixing Rules
Notes: Emphasize complexity

## Slide 7: vdW and PR EoS provide good fits to the experimental data
Optimization Problem
Min
s.t. Mass Balance
Thermodynamics
Decision Variables:
Binary interaction parameters (BIP)
Beta parameters
Parameters:
Temperature, Composition
Critical Properties
[bmim][SCN] [hmim][Cl] [bmim][C1CO2]
[bmim][BF4] [bmim][PF6] [hmim][FAP]
Points – experiments
Lines – model fits
Shiflett, M. and Yokozeki, A. J. Supercritical Fluids, 55(2). (2010).
Morais, A. Harders, A. Baca, K. Olsen, G. Befort, B. Dowling, A. Maginn, E. Shiflett, M. IECR, 59(40). (2020).
,
,
, where and
, where
,
Observations
5-9 fitted parameters
Complicated refrigerant-lubricant mixing rules
Notes: Goal: Reproduce pressure, given temperature and composition
Add back up slide with g-phi method and sensitivity analyses
Shows how we are making adjustments when our old methods can’t help
SAFT: Helmholtz energy residual in terms of hard sphere, chains, association (h-bond) and dispersions
PC-SAFT: used hard chains as the reference fluid and can deal with polar molecules
Soft-SAFT: LJ reference fluid

## Slide 8: vdW and PR EoS provide good fits to the experimental data
[emim][Cl] [hmim][I] [hmim][Br] [pmim][Cl]
[bmim][Cl] [hmim][Cl] [P14,6,6,6][Cl]
Points – experiments
Lines – model fits
Baca, K. Olsen, G. Matamoros Valenciano, L. Bennet, M. Haggard, D. Befort, B. Garciadiego, A. Dowling, W. Maginn, E. Shiflett, M. Sus. Chem. & Engr. (2021)
Observations
1 parameter minimum
Simple vdW mixing rules
Similar goodness of fit to vdW EoS
Optimization Problem
Min
s.t. Mass Balance
Thermodynamics
Decision Variables:
Binary interaction parameters ()
Parameters:
Temperature, Composition
Critical Properties
Notes: Goal: Reproduce pressure, given temperature and composition
Add back up slide with g-phi method and sensitivity analyses
Shows how we are making adjustments when our old methods can’t help
SAFT: Helmholtz energy residual in terms of hard sphere, chains, association (h-bond) and dispersions
PC-SAFT: used hard chains as the reference fluid and can deal with polar molecules
Soft-SAFT: LJ reference fluid

## Slide 9: Thermodynamic modeling enables us to move from data to designs and gain fundamental insights
Monte Carlo Parameter Uncertainty Analysis
Uncertainty Propagation Through Process Model
Observations
Provides insight into
  Parameter correlation
  IL properties
  Expected ranges of process variables
Important for
  Process decisions
  Determining acceptable levels of data and model accuracy
  Understanding molecular and process trade-offs
Morais, A. Harders, A. Baca, K. Olsen, G. Befort, B. Dowling, A. Maginn, E. Shiflett, M. IECR, 59(40). (2020).
IL Critical Point Sensitivity Analyses
Notes: We still have more to do with this thermos modeling work, but this is an example of how we can begin to build insights from multiple design length scales into our data-to-design framework

## Slide 10
Liquid Box
Vapor Box
Experiments
Molecular Simulations
Thermodynamic Modeling & Parameter Estimation
Mullen, Corcelli & Maginn (2018), : J. Phys. Chem. Lett.
Turnaoglu, Ritchie & Shiflett (2019), J. Chem. Eng. Data
Shiflett, M. B. and Yokozeki, A. Chimica Oggi - Chemistry Today, 24(2). (2006).
Thermophysical Property Targets & IL Design
Process Design
Technoeconomic
Analysis
Temperature
Recovery Fraction
Our data-to-design framework enables exploration of how thermodynamic modeling can guide experimental decisions
Questions
Can we use traditional statistical methods to rigorously determine which thermodynamic model to use?
Can this analysis inform experimental collaborators on which data is most important to measure?
Summary
Variety of available data from experimentalists
Multiple thermo models available which give good fits
Choice of thermodynamic model may impact process design and uncertainty results!

## Slide 11: Case study: Peng-Robinson EoS with temperature dependent data
Optimization Problem
Min
s.t. Mass Balance
Thermodynamics
Decision Variables:
Binary interaction parameters ()
Parameters:
Temperature, Composition
Critical Properties
System
HFC-32 solubility in [emim][TF2N]
2 parameters:
Observations
Parameter values decrease as temperature increases
Questions
How do thermodynamic models compare for the same system?
How do thermodynamic models compare between different HFC and IL systems?
Notes: Add GF temp dependence plot to set up
Can combine to 1 equation
Then – how do we evaluate, model selection

## Slide 12: Traditional statistical methods aid in understanding thermodynamic model questions
Claeskens, G. and Hjort, N. Cambridge Books. (2008).
Kramer, S. and Sorensen, H. IEEE Trans. On Automatic Control, 33(2). (1988).
Goal
Quantitatively determine which model best balances complexity and fit
Model Selection
Akaike information criteria (AIC) ranks models by balancing model fit and model parsimony
Maximum likelihood estimate
Number of fitted parameters
Model
Output
Models ranked lowest (best model) to highest (worst model) AIC value
What data is needed from our experimental collaborators?
[emim][Cl]
[hmim][I]
[hmim][Br]
[pmim][Cl]
[bmim][Cl]
[hmim][Cl]
[P14,6,6,6][Cl]
Varying temperature
Multiple ILs at single temperature

## Slide 13: Models Available (Pt. 1)
Model | Number of Parameters | Temperature Dependence | Fitting | Available for HFC-32/[emim][TF2N] | Available for HFC-32/[bmimPF6] | Available for HFC-125/[emim][TF2N]
PR | 1 | None | kij,A | yes | no | yes
PR | 1 | None | kji,A | yes | no | yes
PR | 1 | None | kij,A=-0.05 kji,A | yes | - | -
PR | 2 | None | kij,A kji,A | yes | yes | yes
PR | 3 | Linear | kij,A, kji,A kij,B | yes | yes | yes
PR | 3 | Linear | kij,A, kji,A kji,B | yes | yes | yes
PR | 4 | Linear | kij,A, kji,A kij,B, kji,B | yes | yes | yes
PR | 6 | Quadratic | kij,A, kji,A kij,B, kji,B kij,C, kji,C | yes | yes | yes
PR | 8 | Polynomial | kij,A, kji,A kij,B, kji,B kij,C, kji,C kij,D, kji,D | yes | noo | no
i – HFC
j – IL

## Slide 14: Models Available (Pt. 2)
Model | Number of Parameters | Temperature Dependence | Fitting | Available for HFC-32/[emim][TF2N] | Available for HFC-32/[bmimPF6] | Available for HFC-125/[emim][TF2N]
SRK | 1 | None | kij,A | yes | no | yes
SRK | 1 | None | kji,A | yes | yes | yes
SRK | 2 | None | kij,A kji,A | yes | yes | yes
SRK | 3 | Linear | kij,A, kji,A kij,B | yes | yes | yes
SRK | 3 | Linear | kij,A, kji,A kji,B | yes | yes | yes
SRK | 4 | Linear | kij,A, kji,A kij,B, kji,B | yes | yes | yes
SRK | 6 | Quadratic | kij,A, kji,A kij,B, kji,B kij,C, kji,C | yes | yes | yes
SRK | 8 | Polynomial | kij,A, kji,A kij,B, kji,B kij,C, kji,C kij,D, kji,D | yes | no | no
NRTL | 2 | - |  | TBD | TBD | TBD
i – HFC
j – IL

## Slide 15: Model Selection: HFC-32/[emim][TF2N]
SRK – 8 parameter
SRK – 4 parameter
Observations
SRK + polynomial temperature dependence should be selected
Or, promote SRK (8), SRK (6), PR (6), PR(4) for further study
Experimentalists: Data at multiple temperatures is needed to obtain best fits from thermo models
Objective Units: 1E-9*Pa2

## Slide 16: Different systems give different results
R-32/[bmim][PF6]
R-125/[emim][TF2N]
Observations
We get different results for different systems!
Additional analyses: evaluate optimality metrics, identifiability
Objective Units: 1E-9*Pa2
Notes: + Optimality
+ Identifiability results for now

## Slide 17: Statistical analysis guides model selection for HFC-32/[emim][TF2N] solubility
Observations
Quadratic temperature dependence in the parameters gives both the lowest residual and is ranked 1 by AIC
Experimentalists: Data at multiple temperatures is needed to obtain best fits from thermo models
None
2 Fitted Parameters
Residual: 11.5E3 Pa2
Linear
4 Fitted Parameters
Residual: 0.0451E3 Pa2
Parameter
Temperature Dependence
Quadratic
6 Fitted Parameters
Residual: 0.0439E3 Pa2
Model | AIC | Relative Likelihood | Rank
2 parameter | 13.2 | 0.0011 | 3
4 parameter | 1.41 | 0.39 | 2
6 parameter | -0.483 | 1.0 | 1
Akaike Information Criteria
Notes: 6 parameter is smaller because its MLE is more balance by the number of parameters than the 4 parameter model

## Slide 18
Liquid Box
Vapor Box
Experiments
Molecular Simulations
Thermodynamic Modeling & Parameter Estimation
Mullen, Corcelli & Maginn (2018), : J. Phys. Chem. Lett.
Turnaoglu, Ritchie & Shiflett (2019), J. Chem. Eng. Data
Shiflett, M. B. and Yokozeki, A. Chimica Oggi - Chemistry Today, 24(2). (2006).
Thermophysical Property Targets & IL Design
Process Design
Technoeconomic
Analysis
Temperature
Recovery Fraction
Success story: Data science tools provide experimental guidance
AIC analysis is a straightforward methods to address thermodynamic modeling questions and inform decisions within data-to-design framework

## Slide 19: Exciting opportunities for future work!
Grant No. 1917474
Add in NRTL model
Try Baron
DoE for model discrimination
IL critical property sensitivity analysis
Volatility comparison between models
Notes: As an example, we envision that this will be used in a variety of projects, including further in HFC multiscale engineering applications, such as the one shown here. To this end, ongoing work includes understanding the transferability of our force field to other untuned properties and using this framework to optimize an entire class of HFC molecules. Eventually we plan to integrate this workflow into a computed aided multiscale design scheme for HFC phaseout.

## Slide 20: Exciting opportunities for future work!
Implement automatic model selection in workflow
Determine most important IL properties for efficient separations
Use workflow to provide molecule and process design specifications
Grant No. 1917474
Expand model selection to include other types of thermo models
Notes: As an example, we envision that this will be used in a variety of projects, including further in HFC multiscale engineering applications, such as the one shown here. To this end, ongoing work includes understanding the transferability of our force field to other untuned properties and using this framework to optimize an entire class of HFC molecules. Eventually we plan to integrate this workflow into a computed aided multiscale design scheme for HFC phaseout.

## Slide 21: Acknowledgements
Grant No. 1917474
Maginn Group
Dowling Group
Questions?
Email: bbefort@nd.edu
Shiflett Group